## Slide 1: Uncertainty in condition prediction of bridges based on assessment method – case study in Estonia
Sander Sein, Jose C. Matos, Juhan Idnurm

## Slide 2: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
OUTLINE
Description of the problem
Bridges
Visual inspections
Non-destructive testing
Condition prediction
Conclusions

## Slide 3: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
PROBLEM
Performance of bridges have direct impact on performance of overall road network
Most of the data connected to decision-making is collected with visual inspections
Visual inspections are cost-effective, but based on qualitative method (subjective opinion)
Non-destructive tests are repeatable and have quantitative results, which are difficult to integrate
Does the uncertainty of assessment affect condition preditction?

## Slide 4: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
UNCERTAINTY
Ehrlich, C. (2014). Terminological aspects of the Guide to the Expression of Uncertainty in Measurement (GUM). Metrologia, 51(4), S145–S154.

## Slide 5: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
ESTONIA
Independence declared in 1918
Independence restored in 1991
Area is 45,336 km2
Population is approx. 1,35 million.
Screeshot from maps.google.com

## Slide 6: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
BRIDGE MANAGEMENT IN ESTONIA
  Total number of bridges is approximately 3300
    Estonian Road Administration 1013
    Estonian Railways LTD. 523
    Local authorities approximately 700
    Forest roads ?
    Private roads ?
    Estonian Defense Forces *information not shared

## Slide 7: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
BRIDGE MANAGEMENT IN ESTONIA
National roads
Chart: Age of structures
| 18.century | 19.century | 1900-1909 | 1910-1919 | 1920-1929 | 1930-1939 | 1940-1949 | 1950-1959 | 1960-1969 | 1970-1979 | 1980-1989 | 1990-1999 | 2000-2009 | 2010-2016
Construction year | 1 | 5 | 8 | 4 | 5 | 46 | 30 | 120 | 219 | 140 | 100 | 55 | 115 | 145
Repaired after.1985 | 1 | 5 | 7 | 3 | 4 | 22 | 19 | 72 | 143 | 78 | 42 | 8 | 0 | 0

## Slide 8: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
BRIDGE MANAGEMENT IN ESTONIA
Assessment
Evaluation of element condition (CI)
  Every element is evaluated, unit based
  4 states (1 very good – 4 very poor) without time frame
  Urgent damages with time frame

## Slide 9: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
BRIDGE MANAGEMENT IN ESTONIA
Assessment
BCI (Bridge Condition Index) 0-100%
  Current element value/Total element value=CI
  Different elements have different weight factors
  Overall BCI is calculated based on weighted average
Chart: BCI, %
| 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100
2007 | 3 | 15 | 52 | 155 | 240 | 224 | 197
2016 | 2 | 8 | 35 | 80 | 161 | 184 | 523

## Slide 10: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
TYPICAL BRIDGE OF ESTONIA
Length: 14 m
One span
Built in 1975
Not repaired
Material: reinforced precast concrete
Main girder typology: simply supported beam

## Slide 11: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
BRIDGES UNDER INVESTIGATION
VISUAL INSPECTION
ASSAKU
LAGEDI
SAKU
NON-DESTRUCTIVE TESTING
ALLIKU
KARUTIIGI

## Slide 12: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
ASSAKU
BUILT IN 1970
PRECAST RC
INSPECTED BY EXPERTS
bms.teed.ee

## Slide 13: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
LAGEDI
BUILT IN 1989
PRECAST RC (PRE-STRESSED)
INSPECTED BY EXPERTS
bms.teed.ee

## Slide 14: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
SAKU
BUILT IN 1974
RECONSRUCTED IN 2005
PRECAST RC
INSPECTED BY STUDENTS
bms.teed.ee

## Slide 15: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
VISUAL INSPECTIONS
BCI
Inspector | Lagedi CI | Assaku CI | Saku CI
1 | 48.9 | 66.9 | 49.3
2 | 36.7 | 66.7 | 74.0
3 | 38.2 | 66.8 | 19.3
4 | 36.7 | 87.0 | 76.1
5 | 46.0 | 75.1 | 70.1
6 | 39.8 | 87.0 | -
7 | 55.3 | 88.3 | -
Mean | 43.1 | 76.8 | 57.8
SD | 6.6 | 9,6 | 21,5

## Slide 16: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
NON-DESTRUCTIVE TESTS
EASY
QUICK
Compressive strength of concrete cover according to EVS-EN 12504-2
Carbonation depth according to EVS-EN 14630
Thickness of rebar cover

## Slide 17: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
ALLIKU
BUILT IN 1975
RECONSRUCTED IN 2010
RC SLAB
TESTED BY EXPERTS AND STUDENTS
bms.teed.ee

## Slide 18: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
KARUTIIGI
BUILT IN 1980
RECONSRUCTED IN 2018*
RC SLAB*
TESTED BY EXPERTS
bms.teed.ee

## Slide 19: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
NON-DESTRUCTIVE TESTS
Tester | Rebound value Q | Carbonation depth [mm] | Average cover depth [mm]
E 1 | 66.5 | 9 | 45
E 2 | 67.7 | 8 | 45
S 1 | 66.1 | 6 | 43
S 2 | 63.7 | 7 | 40
S 3 | 64.5 | 7 | 41
S 4 | 62.8 | 7 | 45
S 5 | 63.8 | 6 | 42
S 6 | 67.3 | 7 | 46
S 7 | 66.6 | 7 | 43
S 8 | 65.2 | 7 | 41
Mean | 65.4 | 7.1 | 43.1
SD | 1.6 | 0.83 | 2.0

## Slide 20: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
CONCLUSIONS OF BENCHMARKING
Method | CoV | CoV*4
Visual inspection – students | 0.37 | 1.49
Visual inspection – engineers | 0.15 | 0.61
Visual inspection - experts | 0.13 | 0.50
Rebound hammer | 0.02 | 0.10
Carbonation | 0.12 | 0.47
Cover depth | 0.05 | 0.19

## Slide 21: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
PREDICTIVE MODEL
Continuous-time Markov Process
State-dependent
Time-independent
Discrete transistion
Continuous transistion
Intensity matrix
Instantaneous transition probability

## Slide 22: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
INFERENCE
Bayesian updating with simulation
[Neves, L.C. and Frangopol, D.M, 2005]
Posterior distribution
Likelihood
Standard deviation
Mean value

## Slide 23: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
RESULTS
Students
NDT*
Experts

## Slide 24: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
CONCLUSIONS
Based on the Standard deviation
It is better to inspect bridges
Experienced engineers give more accurate assessment than students
Bridge level assessments are more accurate than element level
Experts are almost as accurate as non-destructive tests
Using NDTs in addition is suggested, but the combination of visual assessment and NDT results should be carefully considered

## Slide 25: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
ACKNOWLEDGEMENT
COST Action TU1406
Archimedes Foundation
Professor Karl Õiger Scholarship Foundation

## Slide 26: Sander Sein, Uncertainty in condition Prediction – Case study in Estonia
THANK YOU FOR YOUR ATTENTION!
sein.sander@taltech.ee